## Slide 2: Side-meeting IETF-124 November 05th, 2024

## Slide 3: Agenda SONiC Overview High-Level Architecture Routing Workgroup Update Virtual Dataplane Workgroup Update Closure

## Slide 4: SONiC Overview

## Slide 5: SONiC/SAI Community and Partners
Merchant Silicon
Switch Platform
Adoption
System/Service

## Slide 6
Goals of SONiC
Disaggregation with
SONiC
Faster
Technology
Evolution
Open &
Modular
Software
Reduce
Operational
Burden
Choices of
Vendors
& Platforms
Notes: And why are we doing SONiC? What are the common goals across so many industry partners in the sonic community?

## Slide 7
2016
2017
2018
2019
2020
2021
2022
Basic L2/L3
Containerized
Fast reboot
RDMA
IPv6
VxLan
Virtualization
Warm Reboot
Streaming Telemetry
EVPN
Kubernetes Mgmt.
configDB
Restful API
100G
ARM support
Chassis
1 G Mgmt. Switch
40G
Smart Cable
PINS
DASH
The Journey so far

## Slide 8: SONiC - Year End Review
380K+
social media reach
27
SONiC members
2024
April
May
June
September
October
SONiC Workshop at
ONE Summit
SONiC China Forum
SONiC Workshop India
4K
active contributors
6
2024 in-person events
SONiC Workshop at
OCP Global Summit
SONiC Workshop Japan
SONiC Workshop at OSS EU

## Slide 9: Workgroups Highlights
AI Workgroup
  Fabric Workstream
    Topology (led by Nvidia, Dell, BRCM, Marvell)
    Routing (led by Nvidia, Dell, BRCM)
  Traffic Management Workstream
    Congestion (led by Nvidia)
    PFC (led by BRCM)
  Telemetry Workstream
  (All workstreams finished first round investigation)
Smart Switch Workgroup
  Platform Architecture HLD for SmartSwitch completed
  DPU database design completed
  Midplane/PCIE architecture completed
  IP address assignment design completion
  gNMI design from NPU to DPU
  DPU High-availability design
  NPU-DPU Health probing design using BFD
OTN Workgroup
  OTN services (OTSS, Syncd-OT, OTAI) HLDs have been reviewed with PR to SONiC.
  OTN virtual platform and KVM device have been supported in SONiC-OTN branch.
  OTN enhancement on sonic-mgmt-common HLD has been reviewed with PR to SONiC.
Routing Workgroup
  Usecases: Phoenix Wing (SRv6), VxLAN-DC, Route Optimization, RIB/FIB, ARS
  Enhanced sonic-mgmt vsonic test infra from single box testing to multi-node topology testing.
  The phoenix wing platform test plan PR and the test infra enhancement code PR are raised.
  Spytest test plan is working in progress between Alibaba team and Cisco team.

## Slide 10: High-Level Architecture
Patrice Brissette, Cisco

## Slide 11: SONiC: Software for Open Networking in the Cloud
مرحبا
你好
Aloha
Bonjour
Hello
Switch Abstraction Interface
नमस्ते
Telemetry
SNMP
BGP
Utility
Mgmt
Switch State Service
1ST party
Platform Management API
PSU
FAN
XCVR
Sensor
LED
Platform/ASIC Independence
Application State Decoupling
Container for serviceability and portability
Rich management capabilities
Notes: What is SONiC

## Slide 12: High-Level Architecture
Documents

## Slide 13: High-Level Architecture
FRRouting

## Slide 14: High-Level Architecture
SONiC Overview

## Slide 15: High-Level Architecture
Spytest

## Slide 16: Useful Links https://github.com/sonic-net/ https://github.com/sonic-net/SONiC/wiki https://github.com/sonic-net/SONiC/wiki/Architecture https://github.com/opencomputeproject/SAI https://frrouting.org/ https://docs.frrouting.org/projects/dev-guide/en/latest/index.html#

## Slide 17: Routing Workgroup Update
Patrice Brissette, Cisco

## Slide 18: Focus Areas and Weekly Discussions
Routing infra related Enhancements and SRv6 related features.
VxLAN Multi-homing
Route download optimization
Adaptive Routing and Switching
SONiC-FRR maintenance
Any routing / forwarding related topics

## Slide 19: VxLAN MH Concept
BD access
L2SVI
(w/ IP)
VRF
L3SVI
(no IP)
BD core
L2VNI
L3VNI
L3 routing
RT-2 (IP), RT-5
Subnet-Stretch
RT-2 (MAC)
BD access
L2SVI
(w/ IP)
VRF
L3SVI
(no IP)
BD core
Host
interface
interface
RT-1 (MW)
RT-4 (ES)
RT-2 (ARP/ND sync)
TOR
TOR

## Slide 20: VxLAN MH Content
VXLAN encapsulation
VXLAN decapsulation
IPv6 and IPv4 VTEP support
Symmetric IRB (L3VNI)
Tunnel Bridge Ports (L2VNI)
  Static MAC
  BUM traffic
Multiple tunnel maps
  VRF per VNI (L3VNI)
  VLAN per VNI (L2VNI)
MAC Mobility
IP Mobility
Static Anycast Gateway
  Support all-active redundancy mode
  Support following features on EVPN MH:
    BUM traffic handling
    Symmetric IRB
    Static Anycast Gateway
    BGP over EVPN Multihomed Ethernet-Segment
    MAC and IP mobility
  Support for Ethernet Segment IDs types
    System-MAC based
    Operator Configured
  Duplicate-Address-Detection
Single-Homed
Multi-Homed

## Slide 21: Adaptive Routing Switching

## Slide 22: Phoenix Wing Initiative
Short Term Goals:
  Verify the deployment readiness of SRv6 solutions via using the SONiC 202411 release on participated hardware devices
Long term goals:
  Promote more SONiC based SRv6 deployments, complete the testing tool set for the SRv6 solutions
    Add SRv6 into SONiC interop lab.
    Provide SONiC SRv6 standardized test cases, set expected test results for SRv6 solutions.
    Offer verfied SRv6 solution deployment scenario cases.
Launched on 05/25/2024 in Beijing, China

## Slide 23: Route Download Optimization
Async mode |  |  | On |  |  |  | On | On | On | On
Multi db |  |  |  | On | On | On | On | On | On | On
Batch / bulk sizes |  |  |  |  | On | On |  | On | On | On
No APPL_STATE_DB population |  | On |  |  | On | On | On | On | On | On
Ring buffer |  |  |  |  | On | On | On | On | On | On
Zmq for ConsumerStateTable |  |  |  |  | On | On |  | On | On | On
No logs |  |  |  |  | On | On |  | On | On | On
Use nexthop groups (even for single nbr) |  |  |  |  |  |  |  |  |  | On
Sort SAI route bulk |  |  |  |  | On | On |  | On | On | On
Bypass saimeta::Meta for bulk operations |  |  |  |  | On | On |  | On | On | On
No APPL_DB and APPL_ASIC_DB populations |  |  |  |  |  | On |  |  | On | On
Total speed (1K routes /sec ) | 2 | 4 | 2.9 | 3.6 | 12 | 13 | 14 | 18.5 | 20.6 | 21
2nd wave: analysis and results
From 2K routes/sec to 21K routes/sec

## Slide 24: Concerns from FRR community
Three problems to be solved in Phoenix Wing
Better Convergence via using Nexthop Group ID
Prefix Independent Convergence (PIC)
SRv6 VPN’s SONiC chain is different from Linux Kernel Chain
FRR team’s concern:
Zebra’s complexity is growing unmanageable.
Recommendation:
Simplify via 'Divide and Conquer’, a.k.a. RIB/FIB separation.

## Slide 25: Routing Stack Building Blocks
Update topology database
Compute optimal path
Converting RIB to FIB
Forwarding chain with
BGP
RIB
PI FIB
PD FIB
HAL
HW
Hardware Abstraction Layer
Download to HW FIB
Common NOS
SONiC
FRRouting BGP
FRRouting Zebra
???
SONiC SDK
SONiC SAI
SONiC Orchagent

## Slide 26: High Level View
zebra
fpmsyncd
APPDB
orchagent
dplane_fpm_sonic.so
zebra
fpmsyncd
APPDB
orchagent
dplane_fpm_sonic.so
SONiC FIB
Before
After
RIB with implicit FIB
RIB
FIB

## Slide 27: Virtual Dataplane Workgroup Update
Murali Venkat, Cisco
Yue Gao, Cisco

## Slide 28
Agenda
SONiC-VPP is a platform under SONiC that supports VPP data plane SONiC-VPP background, features and goals Architecture DC Features(new): Vxlan, SRv6 vSmartswitch with SONiC-VPP & BmV2
SONiC-VPP Testing at Azure Community Collaborations and usage
Call to action
Notes: Why are we doing all this ? What problems are we solving - > Enable a platform for Testing with Traffic on a real dataplane
At Cisco – 2 Complementary solutions – we are doing a open solution and S1 solution …

## Slide 29
Why SONiC-VPP ?
SONiC needs a compelling software forwarding engine, VPP
  Is a real forwarding plane
  Is feature rich & performant
  Is open sourced and community driven
  Runs on commodity hardware
Empowers ANYONE to complete proto to production worthy feature, extensible
No vendor dependency
A new platform for real deployment/usecases over time
Usage Today:
SONiC Development vehicle for DataCenter Testing
In Future:
Cloud Gateways
CellSite router
UPF/Fwa
Stateful Services (Lawful Intercept, IPFix/NF, Fw, LB, Cg-NAT, IPsec etc.)

## Slide 30: VPP – Vector Packet Processor
Extensible and Flexible modular design
Implement as a directed graph of nodes
Extensible with plugins, plugins are equal citizens.
Fully featured dataplane
  L2: VLan, Q-in-Q, Bridge Domains, LLDP .
  L3: IPv4, GRE, VXLAN, DHCP, IPSEC …
  L3: IPv6, Discovery, Segment Routing …
  L4: TCP, UDP …
  CP: API, CLI, IKEv2 …
Performance
V4: 33.5Mpps (22.5Gbps) per core with 64-bytes packets (PDR)
  IPSEC: 3.25Mpps (41.5Gbps) per core with IMIX traffic (PDR)
  Scalable FIB: supporting millions of entries
  0 packet drops, ~15µs latency
Network I/O
Packet Processing: VPP
Management Agent
Netconf/Yang
REST
...
Notes:   DPDK for fast I/O
  ISA: SSE, AVX, AVX2, NEON ..
  IPC: Batching, no mode switching, no context switches, non-blocking
  Multi-core: Cache and memory efficient

## Slide 31: SONiC-VPP Features
Interface/Sub-interface and Stats
L2 Bridging
L3 IPv4/IPv6 – VRF, Route programming
  IPV4/IPV6
  IPV4 Multipath Routing (ECMP)
  BGP
Single-Hop/Multi-hop BFD
LLDP
ACLs
LAG/LACP/PortChannel
VxLAN
SRv6 - Support uN, uA, uDT4/6, H-Encaps and SRv6 policy
202505
202511
202605
Work Group focus:
• Infra related enhancements and features
• Increase test coverage
SONiC
VPP
202502
202506
202510

## Slide 32: SONiC VPP High Level Components
SONIC Control Plane
SONiC VPP SAI
VPP
DPDK
Linux Kernel
Compute/Networking Hardware
IS-IS
MPLS
QOS
Telemetry
SNMPv3
Logging Infra
RESTCONF
SONiC VPP Container/KVM
Streamlined SONiC build on x86
GNMI and REST for all configs including FRR (FRR BGP)
CLI from existing sonic-cli/vpp cli/frr cli – for Manageability & Debuggability
VPP binary api

## Slide 33: SONiC VPP Architecture
Board Support Package / Networking Hardware
Base OS (Choice of Linux Distro)
CPU CLUSTER
CPU CLUSTER
CPU CLUSTER
CPU CLUSTER
Binary API
IPC
platform.json
startup.conf
hwsku.json
ASIC_DB
APPL/
CONFIG
Application Tables
CONFIG Tables
SWSS
SONiC
libsaivpp.so
syncd
VPP workers
VPP Masters
Linux CP plugin
Netlink plugin
VPP
Host Path
Generates
VPP platform service
VM or Container
CLI
GNMI
REST
Notes: Single NPU – could be extended to multiple NPUs​
Up to 32 interfaces – could be extended with different profiles​
10 CPU cores​
VPP control plane:1​
VPP data plane: 3 and can be adjusted based on BW requirements​ to scale up or down – depending on usecase (testing or production)
SONiC: 6​
8G memory​
SONiC-VPP can be deployed in a topology with other physical switchesand/or virtual switches.​
Container deployment is also possible
Platform service generates startup.conf

## Slide 34: SONiC VPP – VNET VxLAN
Support IPv4 and IPv6 VxLAN Encapsulation and Decapsulation for VNET Peering
Support multi-hop BFD monitoring for route protection
VxLAN ECMP path and primary/backup path

## Slide 35: SONiC-VPP SRv6
Supported Behavior | Description
uN | NEXT-CSID (Compressed SID) End behavior with a pseudocode of shift-and-lookup
uA | NEXT-CSID End.X behavior with a pseudocode of shift-and-xconnect (to a specified interface)
SRv6 SID List + Policy | List of segment IDs (SIDs) to be used with traffic steering. Multiple SID lists can be used in a single policy for traffic steering, and both encap and insert are supported (only encap is supported by FRR, however).
Prefix steering over a SID List | Allows for traffic engineering by routing traffic over a pre-defined policy / SID list.
uDT4, uDT6 | Endpoint with decapsulation and IPv4/6 table lookup (IPv6-L3VPN - equivalent to per-VRF VPN label).
Notes: PhoenixWing/Srv6/TE cases can be evaluated in vendor agnostic fashion

## Slide 36: Deployment
SONiC-VPP deployed in a VM
    Single NPU – could be extended to multiple NPUs
    Up to 32 interfaces – could be extended with different profiles
    10 CPU cores
                VPP control plane:1
            VPP data plane: 3 and can be adjusted based on BW requirements
            SONiC: 6
    8G memory
SONiC-VPP can be deployed in a topology with other physical switches and/or virtual switches.
Container deployment is also possible

## Slide 37: vSmartSwitch – SONiC-VPP + Bmv2
A sandbox for smartswitch development & test with all open source components
Solution leverages SONiC-VPP as NPU
Bmv2 simulates DPU data plane
Verification traffic is sent from PTF and sniffed from PTF
SONiC
VPP
BMv2
vSmartSwitch
Notes: It cant be inserted into any Topology
We used it for HA development internally and accelerated our inhouse UT

## Slide 38: SONiC-VPP in Azure
Enable SONiC-VPP as sonic PR checker
Complements SONiC-Vs
Runs nightly
  Build pipelines for 2505 and master (in pass thru mode)
    Test pipeline run sonic-mgmt tests on T1-LAG topology
    Recent test result: 463 passed, 1 unstable
    Additional 500+ ACL tests yet to be committed
    Next Steps
  Promote build and test pipelines to PR checker to both sonic-buildimage and sonic-mgmt
  Expanding to other topos: T0, multi-asic, smartswitch, with more feature coverage
Notes: With CI – we were able to catch a bugs in SONIC Mgmt test which previously went unnoticed …, 1. One case in Fib area 2. SWSS mem usage crossed a threshold causing failure –– we are now able to find more such issues.

## Slide 39: Community Collaborations
SONiC-VPP is​ being evaluated at Equinix to enable hybrid/multi-cloud connectivity, particularly for private networking between Azure, AWS, GCP (and other cloud providers).
This evaluation targets integration of Equinix Fabric, with SONiC and VPP running in containers on Equinix infrastructure as a Service.
This approach allows for quick deployment and teardown, enabling use cases like transferring large datasets between clouds, complying with disaster recovery policies, and enabling multi-modal AI inferencing.
SONiC-VPP is being used to enable AZURE SONiC CI-CD
This approach allows for quick setup, validation and teardown, enabling Azure testing of various technologies, and features in T1 and T0 topologies
SONiC-VPP @
Max & team are making enhancements
to enhance SAI testing using VPP SAI and adding IPinIP

## Slide 40: Roadmap
Phase I
Interfaces and sub interfaces
IPv4, IPv6 routing, adjacencies
VRF and routing protocol support(BGP)
Build system for single container and VM images
Test framework
Phase II
VPP configurability
Debugging support
SONiC-VPP migration to debian bookworm distribution
VPP migration to bookworm release
Loopback interface provisioning
VLAN, port channel (LAG)
ACL(l2,l3) support
Phase III
VxLAN
SRv6
L2 Switching
T1/T0 completion
VPP SAI Unit Test
IPinIP
Container pkg
Memif
STP
QOS, Policer
OSPF, IS-IS
Phase IV
IPsec*
NAT*
Stateful Firewall*
*Dataplane ready

## Slide 41: Call to action ... Next Steps
Open to collaboration and ideas!
Stronger participation in PR reviews, and taking on improvements
Accelerate new features
Completing and onboarding tests on T1/T0 and other topologies
Monitor and triage PR checker failures quickly
Join VirtualDataplane Working Group email:
  virtual-data-plane@lists.sonicfoundation.dev
    Meeting Day: Tue
    Meeting Time: 9am PST
Notes: This is an excellent onboarding/training platform for your teams, so engage them to benefit the community
We are Happy to do more TOIs and Onboard folks and Share VPP Know-how etc
Mindset change ...
Stronger participation in PR review
Getting traction is very difficult
No tool and power to move faster

## Slide 42: Closure
Patrice Brissette, Cisco

## Slide 44: Call for Actions
Participate
  Subscribe to mailing list
  Join the WG meeting and discussions
Contribute
  Participate to challenges, use-cases & new ideas
(Update Incoming Topics)
  HLD & Code PRs
  Reviews
https://lists.sonicfoundation.dev/g/sonic-wg-routing